## Slide 1: ERTS Final Assessment – Task 1 (Template)
Group10:
Xinyi Sun, Zhuoran Xu, Ai Xiao

## Slide 2: Practical elements
Show that the robot can move around effectively in both modes of operations
Show that you have made use of the LED & Switches
Is there any difference in operation when you robot works in polling mode and interrupt mode?
  Polling mode:
    More sensitive for detecting bump pressing.
    Mechanism: Read status of every switch and respond.
  Interrupt mode :
    Due to ISR problem, ignore bump pressing rarely.
    Mechanism: Run main codes continuously but stop to serve needs when interrupt occurs.

## Slide 3: Interrupts
How do you implement operation of robot with polling? Why?
  Use Bump_Read_Input() to detect status.
  Detect bump when it is needed.
How do you implement operation of robot with interrupts? Why?
  Enabling interruption function using port 4 to detect status automatically.
  Monitoring bump all the time.
How have you kept the ISRs minimal?
  Avoid using int or the other long-memory size type.

## Slide 4: Delays
Example | Latency
Example1: start to while(1) function | 48011847
Example2: 66 -67 Polling | 67
Example3:polling (77-78) from checkbumpswitch to case switch | 53
Example3:interaction (77-78) from checkbumpswitch to case switch | 78

## Slide 5: Delays
Where have delays been used? Why?
  Turning Direction
    Make sure movement is stable
  User choose polling or interruption mode
    Make sure the time is enough for the system detecting user’s choice.
  For motor.c:
    Set Duty Cycles.
      Let the output of PWM can be generated continuously within the setting time.

## Slide 6: CPU Usage
How have you measured the CPU utilization?